## Slide 1
VANTIS CORP
Space Situational Awareness Engineering
PAGE 1 OF 2
Orbital Risk Intelligence System (ORIS)
Real-Time Space Debris Collision Assessment & Autonomous Mitigation Platform
TEAM: Engineering — Vantis Corp
PLATFORM: Full-Stack Orbital Analytics & Blockchain Audit System
PREPARED BY: Aayush | July 2026
§
Introduction
Low Earth Orbit is increasingly congested: thousands of active satellites now share space with debris from decades of fragmentation events. The Cosmos 2251 / Iridium 33 collision (2009) and the Fengyun-1C (2007) and Cosmos 1408 (2021) anti-satellite tests alone generated tens of thousands of tracked fragments. Most existing space-situational-awareness tools stop at detection, leaving the maneuver decision — and the paperwork that follows — to human operators, a process too slow for closing-velocity conjunctions.
The Orbital Risk Intelligence System (ORIS) closes that gap. It ingests live Two-Line Element (TLE) sets from CelesTrak, propagates every tracked satellite and debris object using the SGP4 model, and continuously classifies conjunction risk. When a predicted encounter breaches the critical threshold (< 1 km), ORIS does not just alert — it autonomously executes an avoidance-maneuver contract and writes a SHA-256 hash-chained audit block, producing a verifiable, tamper-evident record of the response for mission-control review.
CORE USP — DETECTION → AUTONOMOUS EXECUTION
1
Autonomous Avoidance Triggered
On a CRITICAL breach (< 1 km), ORIS auto-initiates an avoidance-maneuver contract (ORIS-MIT-…) — no operator approval required.
2
Cryptographic Blockchain Ledger
Conjunction state vectors, distance, and timestamp are hashed (SHA-256) into an AuditLog block linked to the previous block via prev_hash.
3
Immutable Incident Register
A permanent record is created in the critical-incident registry for mission-control auditing and post-event review.
§
Methodology
1
Data Ingestion Layer
CelesTrak TLE fetch (httpx) on a 6-hr APScheduler cycle; resilient fallback TLEs; stored via SQLAlchemy (Satellite, Debris, TLERecord) in SQLite.
2
Orbital Propagation
SGP4 model via Skyfield computes GCRS position & velocity vectors for any object at any timestamp.
3
Risk Assessment Engine
Euclidean separation distance → 3-tier classification (CRITICAL / WARNING / SAFE) → multi-hour Time-of-Closest-Approach (TCA) search with confidence grading.
4
Autonomous Response Engine
On CRITICAL breach: incident record created → SHA-256 block chained to previous hash → simulated avoidance-maneuver & insurance contract executed. No human step.
5
Command Dashboard
Next.js 16 + React 19 real-time UI: interactive 3D globe, risk panels, TCA timeline chart, audit-trail explorer.
TECH STACK
FastAPI
SQLAlchemy
Skyfield / SGP4
NumPy
APScheduler
httpx
Next.js 16
React 19
Three.js
Recharts
TypeScript
§
Aim
To design and implement ORIS, a full-stack platform that autonomously ingests orbital element data, predicts conjunction risk between satellites and debris in real time, and — without human intervention — triggers and cryptographically audits an avoidance response the moment risk crosses a critical threshold.
§
Objectives
1
Continuously ingest and refresh TLE catalogs for tracked satellites and debris from CelesTrak via a scheduled background service (6-hour cycle), with resilient fallback TLEs for offline continuity.
2
Propagate precise state vectors (position & velocity) using the SGP4 model in the GCRS reference frame for any tracked object at any timestamp.
3
Classify conjunction risk against distance thresholds (CRITICAL < 1 km, WARNING 1–5 km, SAFE > 5 km) and predict Time of Closest Approach over configurable propagation windows.
4
Build an autonomous critical-response engine that creates incident records and executes simulated avoidance-maneuver and insurance contracts on breach — zero manual steps.
5
Provide an immutable SHA-256 hash-chained audit ledger and an interactive real-time 3D dashboard for mission-control visualization and verification.
6
Expose a documented REST API surface (/assess, /predict, /audit-logs, /incidents) so third-party mission-control tools and future ML-based risk models can integrate directly.
§
Simulation / Experimental Setup
ORIS was validated against a seeded catalog of 8 operational satellites (ISS, Hubble, NOAA-19, Terra, Aqua, Landsat 9, CryoSat 2, Sentinel-6A) and 8 tracked debris objects sourced from real fragmentation events — the Cosmos 2251 / Iridium 33 collision, the Fengyun-1C and Cosmos 1408 ASAT tests, and spent rocket bodies. Resilient fallback TLE sets guarantee propagation continuity even if CelesTrak is unreachable.
SAT
DEB
distance_km → classify_risk()
SAFE >5 km
WARNING 1–5 km
CRITICAL <1 km
Operators select any satellite–debris pair on the dashboard and invoke:
RUN ASSESSMENT — Instantaneous separation distance, relative velocity, and risk classification.
PREDICT TCA — Multi-hour SGP4 propagation sweep to find Time of Closest Approach.
EMERGENCY DRILL — Forces a <1 km encounter to validate the autonomous response pipeline end-to-end.
AUDIT REGISTER — Inspects the SHA-256 hash-chain ledger for tamper-evident verification.
PREDICTION CONFIDENCE GRADING
HIGH
window ≤ 12 h
MEDIUM
window ≤ 24 h
LOW
window > 24 h
Confidence scales with TLE freshness and the length of the propagation window used for TCA prediction.
EMERGENCY DRILL — FORCED BREACH PARAMETERS
simulated_dist_km = 0.3421 km
Debris position offset by (+0.20, +0.20, +0.18) km from the satellite's live propagated state — deterministic, reproducible, always < 1 km.
§
Why ORIS — Traditional SSA vs. ORIS
Capability | Typical SSA Tooling | ORIS
Conjunction detection | Periodic alerts from a screening service | Continuous SGP4-based distance & risk classification, on demand
Response to a critical breach | Manual review → maneuver decision → paperwork | Autonomous avoidance-maneuver contract, executed with zero operator steps
Audit trail | Plain logs / spreadsheets — editable after the fact | SHA-256 hash-chained ledger — cryptographically tamper-evident
Integration surface | Proprietary formats, manual exports | Open documented REST API (/assess, /predict, /audit-logs, /incidents)
Framed against typical pairwise conjunction-screening workflows; ORIS's own pipeline is described in full under Methodology and System Architecture.

## Slide 2
VANTIS CORP
Space Situational Awareness Engineering
PAGE 2 OF 2
Orbital Risk Intelligence System (ORIS)
Real-Time Space Debris Collision Assessment & Autonomous Mitigation Platform
TEAM: Engineering — Vantis Corp
PLATFORM: Full-Stack Orbital Analytics & Blockchain Audit System
PREPARED BY: Aayush | July 2026
§
System Architecture
DATA MODEL — SQLAlchemy ORM (6 entities)
Satellite
Tracked spacecraft — NORAD ID, operator, orbit type.
Debris
Tracked fragments — NORAD ID, source event, orbit type.
TLERecord
Versioned TLE sets per object; indexed on (object_type, norad_id, created_at).
ConjunctionAssessment
Every distance/risk computation, with TCA + confidence when predicted.
CriticalIncident
Autonomous incident record created on breach, with mitigation contract ID.
AuditLog
SHA-256 block_hash / prev_hash chain, tx_hash, verification_status.
REST API SURFACE — FastAPI (/api prefix)
METHOD | PATH | PURPOSE
GET | /satellites | List tracked satellites
GET | /debris | List tracked debris objects
POST | /assess | Real-time distance & risk — auto-triggers response if CRITICAL
POST | /predict | Multi-hour SGP4 TCA sweep — auto-triggers response if CRITICAL
GET | /status | System health, object counts, latest TLE epoch
GET | /incidents | Recent autonomous critical incidents
GET | /audit-logs | SHA-256 chain entries + integrity verification
POST | /simulate-drill | Force a 0.342 km breach to demo the full pipeline
§
Results and Discussion
8
Satellites Tracked
8
Debris Objects Modeled
3-Tier
Risk Model (<1 / 1–5 / >5 km)
SHA-256
Chained Audit Ledger
6-hr
TLE Refresh Cycle
SAMPLE /api/assess OUTPUT — LIVE SGP4 PROPAGATION (current epoch)
Satellite | Debris | Distance (km) | Rel. Velocity (km/s) | Risk
ISS (ZARYA) | COSMOS 2251 DEB | 5,943.99 | 10.901 | SAFE
HUBBLE SPACE TELESCOPE | FENGYUN 1C DEB | 10,724.97 | 9.741 | SAFE
CRYOSAT 2 | COSMOS 1408 DEB | 10,224.70 | 12.127 | SAFE
ISS (ZARYA) | FENGYUN 1C DEB | 8,286.29 | 10.191 | SAFE
EMERGENCY DRILL (forced) | any tracked pair | 0.342 | — | CRITICAL → auto-response
Across every seeded satellite–debris pair, ORIS correctly computed real-time separation distance, relative velocity, and risk classification, and produced TCA timelines whose confidence scales with propagation window and TLE freshness (HIGH ≤ 12 h, MEDIUM ≤ 24 h, LOW beyond). Emergency Drill runs reliably triggered the full autonomous pipeline end-to-end: incident creation, SHA-256 block generation chained to the previous hash, and a simulated avoidance-maneuver contract (ORIS-MIT-XXXXXXXX) complete with computed Δv, fuel cost, and insurance-claim estimate — all without manual intervention. The Audit Register consistently reported chain integrity as VALID, confirming the ledger's tamper-evident design; the 3D dashboard gave mission-control-style visibility into every tracked object, prediction, and autonomous response.
SHA-256 AUDIT CHAIN (AuditLog)
Genesis Block
→
Block #N
prev_hash → block_hash
→
Block #N+1
prev_hash → block_hash
→
Chain Integrity: VALID
§
Summary
Post-collision debris growth and rising Low Earth Orbit traffic density make manual conjunction response too slow for closing-velocity encounters. ORIS is a full-stack Space Situational Awareness platform that ingests live TLE data, propagates orbits with the SGP4 model, and continuously classifies conjunction risk against LEO thresholds. On a critical breach, it autonomously executes an avoidance-maneuver contract and records the action in a SHA-256 hash-chained, tamper-evident audit ledger — closing the loop from detection to verifiable response without human intervention. A documented REST API and an interactive 3D dashboard give mission-control-style visibility and third-party integration into every tracked object, prediction, and autonomous response.
Important References
• Vallado, D. A., Fundamentals of Astrodynamics and Applications, 4th ed. — SGP4/SDP4 orbital propagation theory.
• Rhodes, B., Skyfield Documentation, skyfield.readthedocs.io — astronomy library used for propagation & timescales.
• CelesTrak, “Two-Line Element (TLE) Data Sets,” celestrak.org — live orbital element source for satellite/debris tracking.
• Inter-Agency Space Debris Coordination Committee (IADC), Space Debris Mitigation Guidelines — basis for LEO risk thresholds.
• Kessler, D. J. & Cour-Palais, B. G., "Collision Frequency of Artificial Satellites," J. Geophysical Research, 1978.
• NIST FIPS 180-4, Secure Hash Standard (SHS) — SHA-256 algorithm underlying the immutable audit ledger.
Future Scope
▸ Space-Track.org integration for higher-fidelity TLEs and covariance data beyond CelesTrak's public GP feed.
▸ ML-based probability-of-collision (Pc) scoring from historical conjunction outcomes, replacing fixed distance thresholds.
▸ All-vs-all multi-object conjunction screening for full-catalog coverage, not just pairwise assessment.
▸ Real maneuver-planning integration (e.g. GMAT / AGI STK) to replace the simulated Δv/fuel-cost contract with executable burn plans.